## Slide 1
Presentation 1 recap: how prediction saves bits
The first presentation established the motivation, prediction model, picture roles, and HEVC's main efficiency idea
01 / 49
1
WHY COMPRESS?
Video contains repeated information within and across pictures
2
PREDICT
Intra uses decoded neighbors. Inter reuses blocks from decoded reference pictures
3
SEND THE ERROR
Original − prediction = residual. A better prediction leaves less information to code
4
ORGANIZE PICTURES
I starts independently. P reuses references. B may use references on both sides
5
HEVC'S ADVANTAGE
Flexible block sizes and more prediction choices fit the content more closely
HEVC = High Efficiency Video Coding
Notes: Use this as a one-minute recap of Presentation 1. Video compression works because pictures contain spatial and temporal repetition. Intra prediction uses already decoded neighboring samples, while inter prediction finds a similar block in a decoded reference picture and signals motion information. The encoder sends the residual rather than repeating the original pixels. I, P, and B picture roles organize which references may be used, and the Group of Pictures structure trades compression efficiency against random access and latency. HEVC improves efficiency through larger, more flexible coding blocks and additional prediction choices. Finish with the bridge: this presentation follows the residual through the rest of the HEVC coding loop.
[Slide-specific evidence]
Summary derived from Presentation 1: C:/Users/shara/Desktop/GitHub/H.265/presentation/1_introduction.pptx, especially slides 2–21. Core technical sources: ITU-T Recommendation H.265 and G. J. Sullivan et al., Overview of the High Efficiency Video Coding Standard.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 2
The High Efficiency Video Coding (HEVC) closed loop
The upper path writes the bitstream. The lower path rebuilds the reference picture.
02 / 49
ENCODING PATH
Partition
Predict
Residual
Transform
Quantize
CABAC
Bitstream
Context-Adaptive Binary
Arithmetic Coding
LOCAL RECONSTRUCTION
Reference
picture
Deblocking + Sample
Adaptive Offset (SAO)
Add
prediction
Inverse
transform
Inverse
quantization
quantized coefficients
The encoder contains the same reconstruction steps as the decoder
Matching reference pictures prevent prediction drift
Notes: Read the upper path first. The encoder creates the bitstream. Then return to quantization: the same quantized coefficients travel down through inverse quantization and inverse transform. The encoder adds the prediction, filters the result, and stores the reference picture. The green return arrow feeds that picture into future prediction. This local decoder loop prevents prediction drift.
[Slide-specific evidence]
Chapter 11, Sections 11.1 to 11.4
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 3
From the full picture to Coding Units
First select one Coding Tree Unit, then subdivide that same region into Coding Units
03 / 49
1 FULL PICTURE
BLOCK 1: CTU
The picture contains many Coding Tree Units. Block 1 is the CTU selected for this example.
ZOOM IN
2 BLOCK 1 DIVIDED INTO CUs
SAME CTU
CU LEAVES
The quadtree keeps smooth regions large and can split detailed regions into smaller square CUs.
Open question: which CU split pattern gives the best quality for the required number of bits?
Notes: Start with the full picture on the left. A picture is tiled into Coding Tree Units, and the cyan square marks Block 1, the Coding Tree Unit followed in this presentation. Then move across the zoom arrow. The right image shows the same picture region enlarged. The blue and amber boundaries illustrate its Coding Unit quadtree. At each quadtree node, the encoder either keeps one square Coding Unit or splits it into four equal child Coding Units. Smooth content can remain in a larger Coding Unit, while detailed content may justify smaller Coding Units. Keep the split-selection question open here. The later Rate-Distortion Optimization section explains how an encoder compares legal partitions.
[Slide-specific evidence]
TEXTBOOK.md, Chapter 12, Sections 12.2 and 12.3. Coding Tree Unit and Coding Unit syntax: ITU-T Recommendation H.265.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 4
Prediction Unit (PU): prediction geometry inside a leaf Coding Unit
The CU quadtree creates squares; PU partitions add directional shapes for prediction
Sources and evidence: speaker notes
04 / 49
2N × 2N
2N × N
N × 2N
N × N
Asymmetric Motion
Partition (AMP)
N means half of the Coding Unit width or height
Why CU splitting cannot replace PU shapes
A quadtree split creates four equal squares. Every resulting leaf remains square, so it cannot directly become a rectangular or quarter–three-quarter PU.
Why PU remains separate
A PU selects prediction direction and shape once the leaf CU is fixed, avoiding extra recursive CU splits merely to follow a boundary.
Open Question 2: which legal PU shape and prediction mode give the best rate–quality trade-off?
Notes: Explain why Coding Unit and Prediction Unit are not redundant. Coding Unit recursion divides a square into four equal smaller squares, so every leaf Coding Unit remains square. It cannot directly produce one rectangular or quarter–three-quarter prediction region. A Prediction Unit asks a different question: after the leaf Coding Unit size is fixed, what geometry should share one prediction description? Rectangular and asymmetric options can follow an object or motion boundary without recursively splitting the entire Coding Unit. The square Coding Unit also provides a common parent from which Prediction Unit and Transform Unit structures can vary independently. Restricting the richer prediction shapes to a menu at the leaf avoids multiplying asymmetric recursive choices through the whole Coding Unit tree. Keep the final choice among legal candidates open until Rate-Distortion Optimization.
[Slide-specific evidence]
TEXTBOOK.md, Chapter 12, Sections 12.3 through 12.5, Figures 12.2 through 12.4.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 5
Prediction Unit and Transform Unit answer different questions
Follow one selected Coding Unit through prediction and residual coding
Sources and evidence: speaker notes
05 / 49
SELECTED CU
PREDICTION FROM TWO PUs
PU 1
PU 2
RESIDUAL SPLIT INTO 4 TUs
TU 1
TU 2
TU 3
TU 4
−
=
Bright pixels show a large difference. Dark pixels show a close prediction.
This creates Open Question 3: why does the residual need separate Transform Units instead of reusing the Prediction Unit boundaries?
Notes: Follow the same selected Coding Unit from left to right. The middle image uses two Prediction Units, so the tree side and building side may carry different prediction information. Subtracting prediction from original creates signed residual values. Four Transform Units divide the residual independently of the two-PU boundary. The open question appears directly on this slide: why should transform geometry remain independent from prediction geometry? The later transform-size discussion answers it using the spatial distribution of the residual.
[Slide-specific evidence]
TEXTBOOK.md, Chapter 12, Sections 12.4 to 12.6, Figure 12.4. The selected-CU prediction and residual were derived deterministically from the Block X teaching image.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 6
Block X hierarchy: picture, CTU, CU, PU, and TU
Each panel zooms further into the same example and introduces one coding level
Sources and evidence: speaker notes
06 / 49
1 WHOLE PICTURE
BLOCK 1
2 CTU
ONE CTU
3 CU
SELECTED CU
4 PU
PU 1
PU 2
5 TU
Start with the complete frame and mark Block 1.
Block 1 becomes one Coding Tree Unit.
The CTU quadtree creates square Coding Units.
The selected CU uses two Prediction Units.
Its residual uses four Transform Units.
One frame contains CTUs. Each CTU contains CUs. A leaf CU carries its own PU and TU structures.
Notes: Read the slide from left to right. Begin with the whole source picture and identify Block 1. The second panel enlarges Block 1 as one Coding Tree Unit. The third panel applies the Coding Unit quadtree to that same Coding Tree Unit and highlights one leaf Coding Unit. The fourth panel follows that selected Coding Unit and divides its prediction into two Prediction Units. The fifth panel follows the residual of the same Coding Unit and divides it into four Transform Units. The last two structures serve different jobs: Prediction Units describe prediction geometry, while Transform Units describe transform geometry for the residual.
[Slide-specific evidence]
TEXTBOOK.md, Chapter 12, Sections 12.2 through 12.9. Coding structure: ITU-T Recommendation H.265.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 7
Step 1: collect one signed residual row
The residual equals original luma samples minus predicted luma samples
Sources and evidence: speaker notes
07 / 49
8-SAMPLE EXCERPT
Worked luma example from the highlighted row
ORIGINAL SAMPLES
28
27
25
24
23
22
20
19
minus
PREDICTED SAMPLES
35
32
30
29
28
27
25
24
equals
SIGNED RESIDUAL
-7
-5
-5
-5
-5
-5
-5
-5
−7 means the original sample is 7 levels darker than its prediction.
The Discrete Cosine Transform receives signed residual values, not the grayscale display.
Notes: First select one Transform Unit and one row inside it. The original luma samples and predicted luma samples come from corresponding positions. Subtract prediction from original at every position. This produces the signed residual row minus 7, minus 5, minus 5, minus 5, minus 5, minus 5, minus 5, minus 5. The picture displays magnitude only because negative values cannot be shown directly as ordinary brightness. The numerical row is the data sent into the transform.
[Slide-specific evidence]
Chapter 13, Sections 13.1 and 13.1b. Worked values sampled from the selected teaching image.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 8
Step 2: calculate the Discrete Cosine Transform
Eight spatial residual samples become eight frequency coefficients
Sources and evidence: speaker notes
08 / 49
INPUT RESIDUAL ROW
-7
-5
-5
-5
-5
-5
-5
-5
For each frequency index k = 0 to 7
C[k] = α(k) Σ r[n] cos[π(2n + 1)k / 16]
r[n] is the residual at position n
C[k] measures how strongly frequency pattern k appears
DCT OUTPUT
-14.85
-0.98
-0.92
-0.83
-0.71
-0.56
-0.38
-0.20
k = 0
k = 1
k = 2
k = 3
k = 4
k = 5
k = 6
k = 7
The transform changes the representation. The number of values remains 8.
Notes: Apply the one-dimensional orthonormal Discrete Cosine Transform to the eight signed residual values. For every frequency index k, multiply the residual row by one cosine pattern and add the products. The result contains decimal coefficients: minus 14.85, minus 0.98, minus 0.92, minus 0.83, minus 0.71, minus 0.56, minus 0.38, and minus 0.20. The transform is reversible before quantization and does not reduce eight values to fewer values.
[Slide-specific evidence]
Chapter 13, Sections 13.1b and 13.2. Decimal values use an orthonormal DCT-II for the worked example.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 9
Step 3: interpret the transform coefficients
A nearly constant residual row concentrates energy at low frequency
Sources and evidence: speaker notes
09 / 49
|-14.85|
k = 0
|-0.98|
k = 1
|-0.92|
k = 2
|-0.83|
k = 3
|-0.71|
k = 4
|-0.56|
k = 5
|-0.38|
k = 6
|-0.20|
k = 7
k = 0: Direct Current (DC) coefficient
Represents the average level of the row
Small k: slow changes across the row
Large k: rapid changes and fine detail
One coefficient contains most of the energy. The remaining seven are small.
Notes: The residual row is almost constant: one value is minus 7 and the remaining values are minus 5. The k equals zero Direct Current coefficient therefore dominates. It captures the row's average level. Low-frequency coefficients describe slow changes, while high-frequency coefficients describe rapid alternation. The DCT is useful because correlated samples produce a small number of strong coefficients and many weak coefficients.
[Slide-specific evidence]
Chapter 13, Sections 13.1b, 13.2, and 13.6
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 10
Step 4: QP selects the step, then quantization rounds
Quantization Parameter (QP) controls the divisor used for every transform coefficient
Sources and evidence: speaker notes
10 / 49
1 CHOOSE QP
Encoder policy supplies a QP
2 DERIVE STEP Δ
QP + 6 gives about 2 × Δ
3 QUANTIZE
q = round(C ÷ Δ)
Worked example: use Δ = 2 so the arithmetic stays visible. A real HEVC encoder derives Δ from its chosen QP.
ONE LARGE COEFFICIENT SURVIVES
−14.85 ÷ 2 = −7.425
round to −7
A SMALL COEFFICIENT BECOMES ZERO
−0.98 ÷ 2 = −0.49
round to 0
BEFORE
-14.85 -0.98 -0.92 -0.83 -0.71 -0.56 -0.38 -0.20
AFTER
-7 0 0 0 0 0 0 0
This creates Open Question 4: how does the encoder choose the Quantization Parameter (QP) for a frame or region?
Notes: Start by answering where the divisor comes from. A real HEVC encoder uses a Quantization Parameter, and the quantizer derives the step size from that QP and any scaling-list value. Increasing QP by six approximately doubles the step. This worked example deliberately uses delta equal to two so the arithmetic remains easy to see. Then calculate two coefficients. Minus 14.85 divided by two is minus 7.425, which rounds to minus 7 and survives. Minus 0.98 divided by two is minus 0.49, which rounds to zero. Leave the QP-selection question open here and resolve it later in the rate-control and Rate-Distortion Optimization section.
[Slide-specific evidence]
Chapter 14, Sections 14.1 to 14.4. ITU-T Recommendation H.265 quantization process: https://www.itu.int/rec/T-REC-H.265. The step size of two is pedagogical.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 11
Step 5: the sparse coefficients follow two connected paths
One path writes bits. The other reconstructs the residual that the decoder will use.
Sources and evidence: speaker notes
11 / 49
QUANTIZED COEFFICIENTS
−7 0 0 0
0 0 0 0
BITSTREAM PATH
Context-Adaptive Binary Arithmetic Coding (CABAC)
Next: a fuller five-coefficient example, explained bin by bin
RECONSTRUCTION PATH
DEQUANTIZE
−7 × Δ(2) = −14
INVERSE DISCRETE COSINE TRANSFORM
(IDCT)
RECONSTRUCTED RESIDUAL
−4.95 −4.95 −4.95 −4.95
−4.95 −4.95 −4.95 −4.95
ORIGINAL RESIDUAL
−7 −5 −5 −5 −5 −5 −5 −5
≈
RECONSTRUCTED RESIDUAL
−4.95 at all eight positions
The inverse transform now points directly to its output. The mismatch remains because quantization discarded seven coefficients.
Notes: Begin with the sparse quantized vector and show its two uses. The bitstream path sends coefficients and syntax to Context-Adaptive Binary Arithmetic Coding. The next slide switches to the fuller Block X example with five surviving coefficients so every CABAC stage can be demonstrated. The reconstruction path first dequantizes by multiplying minus seven by the same teaching step of two, producing minus fourteen followed by seven zeros. The arrow then enters the Inverse Discrete Cosine Transform and points directly to the reconstructed residual row. Because only the Direct Current-like coefficient survived, the inverse transform spreads nearly the same value, about minus 4.95, across all eight positions. Quantization caused the mismatch; CABAC itself remains lossless.
[Slide-specific evidence]
Chapters 14 and 15. Reconstruction values use the inverse orthonormal DCT-II for the worked example. CABAC is lossless; quantization caused the information loss.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 12
Step 1: does this transform block contain residual data?
A coded-block flag controls whether the decoder enters residual_coding for this component
Sources and evidence: speaker notes
12 / 49
5
-2
1
0
-1
1
0
0
0
0
0
0
0
0
0
0
LUMA TRANSFORM BLOCK
Does this block contain any nonzero luma coefficient?
YES
cbf_luma = 1
The decoder now parses residual_coding for this luma block
If cbf_luma were 0, no luma coefficient syntax would follow for this transform block.
Notes: Begin with the transform-tree coded-block flag. For the luma component, cbf_luma determines whether residual coefficient syntax is present for this transform block. Block X has nonzero luma coefficients, so cbf_luma is one and the decoder enters residual_coding. If it were zero, the decoder would not try to parse coefficient positions or levels for this luma transform block. Chroma components use their corresponding coded-block flags.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, transform_tree and residual_coding syntax: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 13
Step 2: locate the last significant coefficient
HEVC signals the x and y coordinates of the final nonzero coefficient in scan order
Sources and evidence: speaker notes
13 / 49
1
2
3
4
5
6
7
8
KNOWN TRANSFORM SCAN ORDER
last_sig_coeff_x_prefix
last_sig_coeff_y_prefix
optional x/y suffixes
Result: LastSignificantCoeffX and LastSignificantCoeffY
There is no unary field saying how many significance flags follow.
Notes: This is the first correction to the earlier teaching sequence. HEVC does not transmit a unary count such as one-one-one-one-zero to announce four significance flags. In residual_coding, it first parses last_sig_coeff_x_prefix and last_sig_coeff_y_prefix, followed by suffixes when required. These syntax elements recover the coordinates of the last significant coefficient. The transform size and scan order are already known, so the decoder now knows where reverse scanning begins.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, clause 7.3.8.11 residual_coding: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 14
Step 3: decode coefficient groups and significance
The known scan order—not a delimiter—tells the parser which coefficient position comes next
Sources and evidence: speaker notes
14 / 49
Syntax element | What it answers | When it is used
coded_sub_block_flag | Does this 4×4 coefficient group contain a nonzero? | For applicable groups in larger transform blocks
sig_coeff_flag[x][y] | Is this coefficient position nonzero? | For positions required by residual_coding
inferred significance | This position is already known to be nonzero | At the last-significant position and other specified cases
For Block X: scan backward from the signaled endpoint and build the set of nonzero positions.
Only after that set is known does the parser move to coefficient levels and signs.
Notes: Explain two spatial levels. A transform block is traversed using a specified scan. For applicable coefficient groups, coded_sub_block_flag indicates whether the group contains significant coefficients. Within a coded group, sig_coeff_flag identifies nonzero locations. The last-significant location is already guaranteed nonzero, so its significance can be inferred instead of coded again. The exact presence of a flag is controlled by the residual_coding syntax conditions—not by searching for a special bit pattern.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, clauses 7.3.8.11 and 7.4.9.11: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 15
Open question: how does the decoder separate CABAC fields?
HEVC has a syntax and flag system, but the exact field boundaries remain an open study question
Sources and evidence: speaker notes
15 / 49
Parser is currently requesting | CABAC returns | Meaning of that 1
sig_coeff_flag at position 1 | 1 | this coefficient position is significant
coeff_abs_level_greater1_flag for position 1 | 1 | its absolute level is greater than 1
coeff_sign_flag for position 1 | 1 | its sign is negative
Known so far: the active syntax element gives each decoded bin its meaning.
The decoder never asks: ‘What does this 1 look like?’ It asks: ‘What is the next syntax element?’
Notes: This slide answers the user's exact doubt. CABAC is not handed an undifferentiated string and asked to guess boundaries. The HEVC syntax parser executes residual_coding in a defined order. At each step it requests a particular syntax element, selects the element's context or bypass mode and binarization rule, and asks the arithmetic decoder for the required bin or bins. Therefore a one returned for sig_coeff_flag means significant, while a later one returned for coeff_abs_level_greater1_flag means magnitude greater than one. Their identical value creates no ambiguity because the parser is in a different state.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, residual_coding syntax and CABAC parsing process: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 16
Step 4: decode each significant coefficient level
HEVC uses named level syntax—not a universal greater-than-1, greater-than-2 code for every value
Sources and evidence: speaker notes
16 / 49
Syntax element | Meaning | Coding detail
coeff_abs_level_greater1_flag[n] | Is the absolute level greater than 1? | Context-coded when present
coeff_abs_level_greater2_flag[n] | Is the selected absolute level greater than 2? | Context-coded when present
coeff_sign_flag[n] | 0 = positive; 1 = negative | CABAC bypass mode; may be inferred with sign hiding
coeff_abs_level_remaining[n] | Carries any required remaining magnitude | Adaptive Golomb–Rice binarization
Final level = (remaining + baseLevel) × sign
Which flags are present depends on HEVC's syntax state; it is not a free-standing prefix code.
Notes: Correct the earlier oversimplification. HEVC uses coeff_abs_level_greater1_flag, conditionally coeff_abs_level_greater2_flag, coeff_abs_level_remaining, and coeff_sign_flag. However, not every significant coefficient necessarily carries both greater flags: the syntax maintains counters and presence conditions within each coefficient group. The remaining level uses adaptive Golomb–Rice binarization. Sign flags are bypass-coded and sign-data hiding can infer one sign under specified conditions. For a first presentation, emphasize the roles and the conditional nature instead of claiming a fixed raw bit group for every coefficient.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 17
The actual HEVC residual syntax order
The grammar tells the decoder what each next CABAC decision represents
Sources and evidence: speaker notes
17 / 49
1
cbf_luma / chroma coded-block flags
2
last significant x/y prefix and optional suffix
3
coded sub-block flags and significance flags
4
greater1 / conditional greater2 level flags
5
sign flags and remaining absolute levels
This is a syntax sequence—not one universal literal bit string for every block.
Notes: Walk down the grammar. The coded-block flags determine whether residual_coding is entered. The last-significant coordinate establishes the scan endpoint. Coefficient-group and significance syntax establishes locations. Level and sign syntax establishes values. This ordering is what separates fields. A literal output bit string cannot be derived from Block X's five coefficient values alone because CABAC output also depends on transform size, scan mode, neighboring syntax, context states, slice initialization, and arithmetic-coder state.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, transform_tree and residual_coding syntax: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 18
How CABAC serves the syntax parser
Each request arrives with its own binarization rule, context selection, and decoding mode
Sources and evidence: speaker notes
18 / 49
SYNTAX PARSER
requests one named syntax element
BINARIZATION
knows how many decisions may be needed
CONTEXT / BYPASS
selects probability state or equal-probability mode
ARITHMETIC DECODER
returns the next bin and updates state
Returned value goes back to the active syntax element
Parser state and CABAC state advance together
Notes: Present this as cooperation between two machines. The syntax parser knows what field is legal next. Binarization tells how that syntax value is represented as one or more bins. Context selection supplies the probability model, or bypass mode is selected. The arithmetic decoder returns a bin and updates its state. The parser consumes that bin for the active syntax element, then moves to the next rule. This is why no separator is needed between a significance one and a level one.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, clause 9.3 CABAC parsing process: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 19
How the decoder reconstructs the coefficient block
It retraces the prescribed grammar; it never searches the stream for visual separators
Sources and evidence: speaker notes
19 / 49
1
Read coded-block flag; enter residual_coding only when required
2
Recover the last-significant x/y coordinate
3
Follow the known reverse scan and recover significant positions
4
For those positions, recover levels and signs under the syntax conditions
5
Place each signed level at its known (x, y) coordinate; all others are zero
No count field. No guess from the bit value. No ambiguity.
Notes: Close the corrected section by narrating the decoder. It follows the normative order and conditions, so it knows whether it is decoding a location, a significance decision, a greater-than-level flag, a remaining level, or a sign. The exact same numerical bin may occur in all of these roles. Its interpretation is supplied by the active syntax rule. The old hypothetical unary count, arithmetic probability table, floating-point tag, and claimed 22-bit output have therefore been removed from the main deck.
[Slide-specific evidence]
Normative source: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3: https://www.itu.int/rec/dologin_pub.asp?id=T-REC-H.265-201906-S%21%21PDF-E&lang=e&type=items
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 20
Arithmetic encoding: bins 1 to 10
Split = low + width × P(0). Bin 1 keeps the upper interval. Bin 0 keeps the lower interval.
Sources and evidence: speaker notes
20 / 49
# | Meaning | Bin | P(0) | Low | High | Width | Split | Resulting interval
1 | coded-block presence | 1 | 0.15 | 0.00000 | 1.00000 | 1.00000 | 0.15000 | [0.15000, 1.00000)
2 | significance: position 1 | 1 | 0.10 | 0.15000 | 1.00000 | 0.85000 | 0.23500 | [0.23500, 1.00000)
3 | significance: position 2 | 1 | 0.25 | 0.23500 | 1.00000 | 0.76500 | 0.42625 | [0.42625, 1.00000)
4 | significance: position 3 | 1 | 0.45 | 0.42625 | 1.00000 | 0.57375 | 0.68444 | [0.68444, 1.00000)
5 | significance: position 4 | 1 | 0.55 | 0.68444 | 1.00000 | 0.31556 | 0.85800 | [0.85800, 1.00000)
6 | position 1 magnitude > 1 | 1 | 0.50 | 0.85800 | 1.00000 | 0.14200 | 0.92900 | [0.92900, 1.00000)
7 | position 1 magnitude > 2 | 1 | 0.50 | 0.92900 | 1.00000 | 0.07100 | 0.96450 | [0.96450, 1.00000)
8 | position 1 remainder a | 1 | 0.50 | 0.96450 | 1.00000 | 0.03550 | 0.98225 | [0.98225, 1.00000)
9 | position 1 remainder b | 0 | 0.50 | 0.98225 | 1.00000 | 0.01775 | 0.99112 | [0.98225, 0.99112)
10 | position 1 sign | 0 | 0.50 | 0.98225 | 0.99112 | 0.00888 | 0.98669 | [0.98225, 0.98669)
Interval after bin 10: [0.98225, 0.98669)
Notes: For each row, calculate the current width, split the interval using P of zero, and retain the subinterval selected by the supplied bin. The second table continues from the first without restarting. After bin nineteen, the worked interval is approximately zero point nine eight five three six to zero point nine eight five three eight.
Sources: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3; V. Sze and D. Marpe, Entropy Coding in HEVC. The displayed 19-bin sequence and decimal probabilities are a teaching calculation supplied for this presentation, not a captured conforming HEVC bitstream.

## Slide 21
Arithmetic encoding table, continued
Split = low + width × P(0). Bin 1 keeps the upper interval. Bin 0 keeps the lower interval.
Sources and evidence: speaker notes
21 / 49
# | Meaning | Bin | P(0) | Low | High | Width | Split | Resulting interval
11 | position 2 magnitude > 1 | 1 | 0.55 | 0.98225 | 0.98669 | 0.00444 | 0.98469 | [0.98469, 0.98669)
12 | position 2 magnitude > 2 | 0 | 0.60 | 0.98469 | 0.98669 | 0.00200 | 0.98589 | [0.98469, 0.98589)
13 | position 2 sign | 1 | 0.50 | 0.98469 | 0.98589 | 0.00120 | 0.98529 | [0.98529, 0.98589)
14 | position 3 magnitude > 1 | 0 | 0.65 | 0.98529 | 0.98589 | 0.00060 | 0.98568 | [0.98529, 0.98568)
15 | position 3 sign | 0 | 0.50 | 0.98529 | 0.98568 | 0.00039 | 0.98548 | [0.98529, 0.98548)
16 | position 4 magnitude > 1 | 0 | 0.70 | 0.98529 | 0.98548 | 0.00019 | 0.98543 | [0.98529, 0.98543)
17 | position 4 sign | 1 | 0.50 | 0.98529 | 0.98543 | 0.00014 | 0.98536 | [0.98536, 0.98543)
18 | position 5 magnitude > 1 | 0 | 0.75 | 0.98536 | 0.98543 | 0.00007 | 0.98541 | [0.98536, 0.98541)
19 | position 5 sign | 0 | 0.50 | 0.98536 | 0.98541 | 0.00005 | 0.98538 | [0.98536, 0.98538)
Interval after bin 19: [0.98536, 0.98538)
Notes: For each row, calculate the current width, split the interval using P of zero, and retain the subinterval selected by the supplied bin. The second table continues from the first without restarting. After bin nineteen, the worked interval is approximately zero point nine eight five three six to zero point nine eight five three eight.
Sources: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3; V. Sze and D. Marpe, Entropy Coding in HEVC. The displayed 19-bin sequence and decimal probabilities are a teaching calculation supplied for this presentation, not a captured conforming HEVC bitstream.

## Slide 22
Binary-tag search: bisection steps 1 to 8
Target interval: [0.98536, 0.98538). Repeatedly bisect the candidate range.
Sources and evidence: speaker notes
22 / 49
Step | Candidate range | Midpoint | Target location | Bit | New candidate range
1 | [0, 1) | 0.5 | above | 1 | [0.5, 1)
2 | [0.5, 1) | 0.75 | above | 1 | [0.75, 1)
3 | [0.75, 1) | 0.875 | above | 1 | [0.875, 1)
4 | [0.875, 1) | 0.9375 | above | 1 | [0.9375, 1)
5 | [0.9375, 1) | 0.96875 | above | 1 | [0.96875, 1)
6 | [0.96875, 1) | 0.984375 | above | 1 | [0.984375, 1)
7 | [0.984375, 1) | 0.9921875 | below | 0 | [0.984375, 0.9921875)
8 | [0.984375, 0.9921875) | 0.98828125 | below | 0 | [0.984375, 0.98828125)
Bits after step 8: 11111100
Notes: This table converts the final arithmetic interval into a binary tag using bisection. For steps one through six the target lies above the midpoint, so append one and keep the upper half. Steps seven and eight append zero and keep the lower half.
Sources: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3; V. Sze and D. Marpe, Entropy Coding in HEVC. The displayed 19-bin sequence and decimal probabilities are a teaching calculation supplied for this presentation, not a captured conforming HEVC bitstream.

## Slide 23
Binary-tag search, continued
The 16-bit point lies inside the target. A 17-bit prefix gives a fully contained binary cell.
Sources and evidence: speaker notes
23 / 49
Step | Candidate range | Midpoint | Decision | Bit | Result
9 | [0.984375, 0.98828125) | 0.98632813 | below | 0 | lower half
10 | [0.984375, 0.98632813) | 0.98535156 | above | 1 | upper half
11 | [0.98535156, 0.98632813) | 0.98583984 | below | 0 | lower half
12 | [0.98535156, 0.98583984) | 0.98559570 | below | 0 | lower half
13 | [0.98535156, 0.98559570) | 0.98547363 | below | 0 | lower half
14 | [0.98535156, 0.98547363) | 0.98541260 | below | 0 | lower half
15 | [0.98535156, 0.98541260) | 0.98538208 | below | 0 | lower half
16 | [0.98535156, 0.98538208) | 0.98536682 | midpoint is inside | 1 | valid tag point
17 | append 0 to the 16-bit tag | — | contained prefix cell | 0 | [0.98536682, 0.98537445)
16-bit tag point: 1111110001000001
17-bit contained prefix: 11111100010000010
Real HEVC CABAC emits integer-coded bits incrementally. This bisection is the teaching model for the supplied interval.
Notes: Continue the binary tag calculation. The sixteen-bit binary fraction evaluates to approximately zero point nine eight five three six six eight and lies inside the final target interval. The complete sixteen-bit dyadic cell is not fully contained. Appending zero gives the seventeen-bit prefix cell from approximately zero point nine eight five three six six eight two to zero point nine eight five three seven four four five, which is fully inside. Keep the distinction between an idealized tag calculation and the normative integer CABAC engine.
Sources: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3; V. Sze and D. Marpe, Entropy Coding in HEVC. The displayed 19-bin sequence and decimal probabilities are a teaching calculation supplied for this presentation, not a captured conforming HEVC bitstream.

## Slide 24
Inverse arithmetic decoding: bins 1 to 10
Use the same split points. Compare R = 0.9853668 with each split and retrace the encoding path.
Sources and evidence: speaker notes
24 / 49
# | Meaning | Split | R ≥ split? | Recovered bin | Narrowed interval
1 | coded-block presence | 0.15000 | yes | 1 | [0.15000, 1.00000)
2 | significance: position 1 | 0.23500 | yes | 1 | [0.23500, 1.00000)
3 | significance: position 2 | 0.42625 | yes | 1 | [0.42625, 1.00000)
4 | significance: position 3 | 0.68444 | yes | 1 | [0.68444, 1.00000)
5 | significance: position 4 | 0.85800 | yes | 1 | [0.85800, 1.00000)
6 | position 1 magnitude > 1 | 0.92900 | yes | 1 | [0.92900, 1.00000)
7 | position 1 magnitude > 2 | 0.96450 | yes | 1 | [0.96450, 1.00000)
8 | position 1 remainder a | 0.98225 | yes | 1 | [0.98225, 1.00000)
9 | position 1 remainder b | 0.99112 | no | 0 | [0.98225, 0.99112)
10 | position 1 sign | 0.98669 | no | 0 | [0.98225, 0.98669)
Recovered first 10 bins: 1111111100
Notes: This is the deconstruction or decoding table. At each step, compare the selected tag value with the same split point used during encoding. If the tag lies above the split, recover one and retain the upper interval. Otherwise recover zero and retain the lower interval. Because the tag lies inside the final nested interval, all nineteen supplied bins are recovered in the original order.
Sources: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3; V. Sze and D. Marpe, Entropy Coding in HEVC. The displayed 19-bin sequence and decimal probabilities are a teaching calculation supplied for this presentation, not a captured conforming HEVC bitstream.

## Slide 25
Inverse arithmetic decoding, continued
Use the same split points. Compare R = 0.9853668 with each split and retrace the encoding path.
Sources and evidence: speaker notes
25 / 49
# | Meaning | Split | R ≥ split? | Recovered bin | Narrowed interval
11 | position 2 magnitude > 1 | 0.98469 | yes | 1 | [0.98469, 0.98669)
12 | position 2 magnitude > 2 | 0.98589 | no | 0 | [0.98469, 0.98589)
13 | position 2 sign | 0.98529 | yes | 1 | [0.98529, 0.98589)
14 | position 3 magnitude > 1 | 0.98568 | no | 0 | [0.98529, 0.98568)
15 | position 3 sign | 0.98548 | no | 0 | [0.98529, 0.98548)
16 | position 4 magnitude > 1 | 0.98543 | no | 0 | [0.98529, 0.98543)
17 | position 4 sign | 0.98536 | yes | 1 | [0.98536, 0.98543)
18 | position 5 magnitude > 1 | 0.98541 | no | 0 | [0.98536, 0.98541)
19 | position 5 sign | 0.98538 | no | 0 | [0.98536, 0.98538)
Recovered all 19 bins: 1111111100101000100
Notes: This is the deconstruction or decoding table. At each step, compare the selected tag value with the same split point used during encoding. If the tag lies above the split, recover one and retain the upper interval. Otherwise recover zero and retain the lower interval. Because the tag lies inside the final nested interval, all nineteen supplied bins are recovered in the original order.
Sources: ITU-T Recommendation H.265, clauses 7.3.8.11, 7.4.9.11, and 9.3; V. Sze and D. Marpe, Entropy Coding in HEVC. The displayed 19-bin sequence and decimal probabilities are a teaching calculation supplied for this presentation, not a captured conforming HEVC bitstream.

## Slide 26
CABAC and reconstruction are separate branches
Both branches start from the same quantized coefficients and serve different purposes
Sources and evidence: speaker notes
26 / 49
BLOCK X QUANTIZED COEFFICIENTS
5
-2
1
0
-1
1
0
0
0
0
0
0
0
0
0
0
same starting data
BITSTREAM BRANCH
Context-Adaptive Binary Arithmetic Coding (CABAC)
Coded syntax bins
→ bitstream payload
The encoder transmits this branch. It does not feed the filters.
RECONSTRUCTION BRANCH
DEQUANTIZE
INVERSE
TRANSFORM
ADD
PREDICTION
DEBLOCK +
SAMPLE ADAPTIVE
OFFSET (SAO)
STORE
REFERENCE
No arrow connects CABAC to filtering. The branches only share the quantized coefficients and syntax decisions.
Notes: CABAC finishes the bitstream branch by coding the syntax bins produced under the normative grammar. Do not claim a literal Block X bit string here: the exact output also depends on the full syntax context and arithmetic-coder state. The reconstruction branch independently takes the same quantized coefficients, dequantizes them, applies the inverse transform, adds the prediction, filters the reconstructed samples, and stores them for future prediction. CABAC does not feed deblocking or Sample Adaptive Offset. Both branches remain decoder-consistent because the decoder receives the coded syntax and reproduces the reconstruction branch.
[Slide-specific evidence]
Closed-loop encoder structure and CABAC: ITU-T Recommendation H.265: https://www.itu.int/rec/T-REC-H.265; G. J. Sullivan et al., Overview of the HEVC Standard: https://doi.org/10.1109/TCSVT.2012.2221191
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 27
Block X dequantization restores coefficient scale, not lost detail
Quantization used step size 8. Dequantization multiplies every transmitted level by 8.
Sources and evidence: speaker notes
27 / 49
ORIGINAL TRANSFORM COEFFICIENTS
42
-12
4
1
-9
5
-2
0
3
-1
1
0
1
0
0
0
QUANTIZE
÷ 8 AND ROUND
QUANTIZED LEVELS
5
-2
1
0
-1
1
0
0
0
0
0
0
0
0
0
0
DEQUANTIZE
× 8
DEQUANTIZED COEFFICIENTS
40
-16
8
0
-8
8
0
0
0
0
0
0
0
0
0
0
42 became 40 −12 became −16 4 became 8 Small coefficients became 0
Dequantization recovers scale. It cannot recover values discarded by rounding.
Notes: Use the exact Block X numbers. Quantization with step eight maps the original coefficients to five nonzero levels. Dequantization multiplies those levels by eight, producing 40, minus 16, 8, minus 8, and 8. These values approximate the original coefficients but do not equal them. Values such as 42 and minus 12 changed, and small coefficients disappeared entirely. This is why the reconstruction remains close to the original but cannot be identical.
[Slide-specific evidence]
Chapter 14; supplied Block X coefficient matrices.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 28
Inverse transform and prediction reconstruct Block X pixels
The decoder performs the same inverse operations and obtains the same reconstructed block
Sources and evidence: speaker notes
28 / 49
DEQUANTIZED COEFFICIENTS
40 −16 8 0
−8 8 0 0
remaining values = 0
INVERSE TRANSFORM
SIGNED RECONSTRUCTED RESIDUAL*
+
=
PREDICTION
SIGNED RESIDUAL*
RECONSTRUCTED PIXELS
*Residual images display magnitude for visibility. The addition uses signed sample values.
Notes: The inverse transform converts Block X's dequantized frequency coefficients back into a signed residual block. Add that residual to the prediction sample by sample. The result is the reconstructed Block X that both encoder and decoder possess. The residual panels show magnitude so the structure remains visible, but the actual arithmetic uses positive and negative residual samples. The next two slides filter these reconstructed pixels before storing the picture as a future reference.
[Slide-specific evidence]
Chapter 11, reconstruction loop; supplied Block X visual sequence.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 29
Deblocking distinguishes coding seams from real image edges
A large sample jump does not automatically mean that the filter should smooth it
Sources and evidence: speaker notes
29 / 49
candidate coded boundary
ARTIFICIAL CODING SEAM
Independent blocks reconstruct slightly different levels
before
96
98
111
109
jump = 13
after
96
101
106
109
jump = 5
GENUINE SCENE EDGE
52 55
172 176
The building edge explains this jump, so filtering stays weak or turns off.
Deblocking smooths an artificial seam at a coded boundary while preserving a real edge in the scene.
Notes: First point to the grid: these are candidate Coding Unit or Transform Unit boundaries. Then use the numeric seam. Independent coding produced a jump from 98 to 111 exactly at the boundary, even though the underlying area should vary smoothly. Deblocking adjusts only nearby samples and reduces that jump. Contrast this with the genuine building edge, where the jump from about 55 to 172 corresponds to real content. Local gradients and boundary strength keep filtering weak or disabled there. The numbers are a simplified teaching example, not measured values from the photograph.
[Slide-specific evidence]
Chapter 16, deblocking filter. ITU-T Recommendation H.265 in-loop deblocking process. Numeric values are illustrative.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 30
SAO corrects reconstruction error away from block boundaries
Deblocking removes coding seams. Sample Adaptive Offset (SAO) corrects sample bias that remains inside a region.
Sources and evidence: speaker notes
30 / 49
INTERIOR SAMPLES
AFTER DEBLOCKING
No coded boundary passes through the highlighted samples
ERRORS STILL REMAIN INSIDE THE BLOCK
Original
After deblocking
Error
140
150
140
135
145
141
154
139
131
144
+1
+4
-1
-4
-1
154 is 4 too high
131 is 4 too low
SAO: 154 − 4 = 150
SAO: 131 + 4 = 135
Deblocking cannot fix these samples because they are not a boundary discontinuity.
SAO classifies the reconstructed samples and applies signaled offsets.
Notes: This slide explains why Sample Adaptive Offset remains necessary after deblocking. The example samples lie inside a coded region, so no artificial block seam exists for the deblocking filter to target. Quantization and reconstruction still left one peak four levels too high and one valley four levels too low. The encoder measures this bias using the original picture and signals SAO parameters. The decoder uses reconstructed neighbors or intensity bands to reproduce the classification, then applies the signaled offsets. The numbers are a simplified teaching example.
[Slide-specific evidence]
Supplied Complete SAO Process, Sections 1 and 2. ITU-T Recommendation H.265, Sample Adaptive Offset process. Numeric values are illustrative.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 31
Edge Offset classifies samples by local shape
One direction applies across the region, and every reconstructed sample enters one of five categories
Sources and evidence: speaker notes
31 / 49
ONE OF FOUR DIRECTIONS
0°
90°
135°
45°
The encoder chooses one direction and signals it for Edge Offset.
Category | Condition comparing c with a and b | Local shape
1 | c < a and c < b | valley
2 | one comparison is < and the other is = | concave corner
3 | one comparison is > and the other is = | convex corner
4 | c > a and c > b | peak
0 | none of the above | no offset
Classification uses reconstructed samples only, because the decoder never has the original picture.
Notes: Edge Offset first selects one of four directions: horizontal, vertical, or either diagonal. For each reconstructed sample c, the decoder compares c with two neighbors a and b along that direction. The comparisons place the sample into valley, concave-corner, convex-corner, peak, or category zero. Category zero receives no correction. The classification cannot use the source picture because only the encoder has it; the decoder must reproduce the category from reconstructed samples alone.
[Slide-specific evidence]
Supplied Complete SAO Process, Section 3a. ITU-T Recommendation H.265, Edge Offset classification.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 32
Edge Offset uses fixed signs that only smooth
The bitstream carries four magnitudes. The standard determines each category's sign.
Sources and evidence: speaker notes
32 / 49
POSITIVE OFFSETS
Category 1: valley
Category 2: concave corner
raise low samples
+ magnitude
NEGATIVE OFFSETS
Category 3: convex corner
Category 4: peak
lower high samples
− magnitude
Category 0 always uses offset 0
The sign is not transmitted. Reversing these signs would sharpen the edge, which Edge Offset does not permit.
Notes: For Edge Offset, the encoder signals one magnitude for each nonzero category, but it does not signal a sign. Categories one and two always use positive offsets, lifting valleys and concave corners. Categories three and four always use negative offsets, reducing convex corners and peaks. Category zero always receives zero. This fixed-sign rule makes Edge Offset a smoothing correction rather than a sharpening tool.
[Slide-specific evidence]
Supplied Complete SAO Process, Section 3a. ITU-T Recommendation H.265, Edge Offset signs.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 33
Band Offset classifies samples by intensity
For 8-bit video, the range 0 to 255 is divided into 32 bands of eight values each
Sources and evidence: speaker notes
33 / 49
band k contains values from 8k through 8k + 7
0
4
8
12
16
20
24
28
0
255
four consecutive selected bands
Classification
Use the sample's own value. No neighbor comparison is needed.
Signaling
Signal the starting band and offsets for four adjacent bands.
Offset sign
Band Offset may use positive or negative offsets.
Samples outside the selected four-band window receive offset 0.
Notes: Band Offset does not compare neighbors. For 8-bit samples, it divides values zero through 255 into 32 equal bands, each eight values wide. The encoder selects a window of four consecutive bands and signals its starting index plus four offsets. Samples outside those bands receive zero. Unlike Edge Offset, Band Offset permits either offset sign because its correction follows intensity bias rather than local peak-and-valley shape.
[Slide-specific evidence]
Supplied Complete SAO Process, Section 3b. ITU-T Recommendation H.265, Band Offset classification.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 34
SAO parameters are signaled for each Coding Tree Block
A Coding Tree Block is the per-component part of a Coding Tree Unit
Sources and evidence: speaker notes
34 / 49
SIGNAL ONCE FOR THE REGION
1
SAO off, Edge Offset, or Band Offset
2
Edge direction or Band Offset starting band
3
Up to four offset magnitudes
MERGE WITH A NEIGHBOR
CTU 1
CTU 2
CTU 3
CTU 4
CTU 5
CTU 6
←
↑
merge left
or merge up
Merging reuses a processed neighbor's SAO parameters and avoids sending a new parameter set.
Notes: HEVC signals Sample Adaptive Offset parameters at Coding Tree Block granularity, meaning separately for the component blocks within a Coding Tree Unit. The syntax identifies whether SAO is off, Edge Offset, or Band Offset. Edge Offset adds a direction; Band Offset adds a starting band. Both modes can signal up to four magnitudes. A block may instead merge with its left or upper neighbor and reuse that neighbor's SAO parameters, reducing syntax cost when nearby regions need similar correction.
[Slide-specific evidence]
Supplied Complete SAO Process, Section 4. ITU-T Recommendation H.265, SAO parameter and merge syntax.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 35
The encoder chooses SAO parameters, and the decoder applies them
Only the encoder sees the original picture. Both sides share the reconstructed picture and signaled parameters.
Sources and evidence: speaker notes
35 / 49
ENCODER
Has original + reconstructed samples
Tests SAO off, Edge Offset directions, and Band Offset windows
Measures distortion reduction and signaling cost
chooses type, direction or band, and offsets
DECODER
Has reconstructed samples + bitstream
Reads the signaled parameters and classifies samples using reconstructed data
Looks up the category offset and adds it
produces the same filtered samples
SAO syntax
The standard defines what the decoder applies. Encoder search strategy remains an implementation choice.
Notes: Separate the responsibilities clearly. The encoder compares reconstructed samples with the true source, tests candidate SAO parameters, and can use the rate-distortion cost J equals D plus lambda R to balance correction benefit against signaling bits. HEVC does not prescribe the encoder's exact search strategy. The decoder never sees the original. It reads the selected parameters, classifies reconstructed samples, and adds the corresponding offsets. Both sides therefore generate identical filtered references.
[Slide-specific evidence]
Supplied Complete SAO Process, Section 5. ITU-T Recommendation H.265 defines decoder behavior and bitstream syntax, not a mandatory encoder search algorithm.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 36
Block X Edge Offset example
The encoder selects horizontal Edge Offset for this teaching CTU and signals magnitude 4 for peak and valley categories
Sources and evidence: speaker notes
36 / 49
Position | 1 | 2 | 3 | 4 | 5
True sample | 140 | 150 | 140 | 135 | 145
Reconstructed | 141 | 154 | 139 | 131 | 144
EO category | — | 4 peak | 0 | 1 valley | —
Offset | 0 | −4 | 0 | +4 | 0
Filtered output | 141 | 150 | 139 | 135 | 144
Position 2: 154 − 4 = 150 Position 4: 131 + 4 = 135
Position 3 enters category 0, so the decoder leaves 139 unchanged.
Notes: Walk through the complete Block X row. For horizontal Edge Offset, reconstructed value 154 has neighbors 141 and 139. It exceeds both, so it enters category four, the peak category, and receives minus four. Reconstructed value 139 lies between 154 and 131, so it enters category zero and remains unchanged. Reconstructed value 131 is lower than neighbors 139 and 144, so it enters category one, the valley category, and receives plus four. In this teaching example, the corrected peak and valley match their source values exactly. Real results need not be exact.
[Slide-specific evidence]
Supplied Complete SAO Process, Section 6, Block X worked example.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 37
Deblocking and SAO correct different artifacts
The cited experiments use different configurations, so their percentages should not be added
Sources and evidence: speaker notes
37 / 49
DEBLOCKING
Targets discontinuities across coded block boundaries
1.3% average BD-rate penalty
when deblocking was disabled
SAMPLE ADAPTIVE OFFSET
Targets systematic overshoot, undershoot, and intensity bias
about 2% average bitrate reduction
up to about 6% in the reported tests
Do not add the two percentages: each paper used its own anchor, sequence set, and test conditions.
[S5] https://doi.org/10.1109/TCSVT.2012.2223053
[S6] https://doi.org/10.1109/TCSVT.2012.2221529
Notes: Close the filtering section by contrasting the targets and then explain the evidence carefully. Deblocking addresses discontinuities at coded block boundaries. Norkin and colleagues report an average 1.3 percent BD-rate increase when the HEVC deblocking filter is disabled in the cited HM 7.0 experiment. This means the enabled filter supplied approximately that coding-efficiency benefit under those conditions. Fu and colleagues report that Sample Adaptive Offset produced about two percent average bitrate reduction and up to about six percent in their reported simulations. These numbers come from different experiments and must not be added to produce a combined gain. Results vary with test sequences, coding configuration, quality metric, anchor, and software version.
[Slide-specific evidence]
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE Transactions on Circuits and Systems for Video Technology, 22(12), 1746-1754, 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053. [S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE Transactions on Circuits and Systems for Video Technology, 22(12), 1755-1764, 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 38
Rate–Distortion Optimization compares incompatible trade-offs
The same region can be encoded in many legal ways, each with a different bitrate and reconstruction error
Sources and evidence: speaker notes
38 / 49
SAME BLOCK X
A
LARGE CODING UNIT
few flags, weaker prediction
B
SMALLER CODING UNITS
more flags, better prediction
C
DEEP PARTITION TREE
lowest error, highest syntax cost
Best picture quality?
Fewest bits?
These questions can select different candidates.
The encoder needs one score that combines reconstruction error and bit cost.
Notes: Start with the problem, not the formula. A Coding Tree Unit can produce many legal Coding Unit trees, Prediction Unit partitions, prediction modes, and Transform Unit structures. Candidate A may use fewer syntax bits but predict poorly. Candidate C may reconstruct more accurately but spend many bits describing deep partitions and coefficients. The encoder cannot select a candidate by quality alone or by rate alone. Rate-Distortion Optimization supplies one comparable cost. The drawings are schematic and do not enumerate the full HEVC search space.
[Slide-specific evidence]
Chapter 17, Rate-Distortion Optimization. HEVC overview by Sullivan et al., 2012. Candidate diagrams are illustrative.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 39
The Rate–Distortion cost function
Rate–Distortion Optimization (RDO) assigns one comparable cost to every candidate
Sources and evidence: speaker notes
39 / 49
J = D + λR
LOWEST J WINS
D
DISTORTION
Difference between the original and reconstructed samples
R
RATE
Bits for partition flags, modes, motion data, coefficients, and other syntax
λ
LAMBDA
Exchange rate between distortion units and bits
1
Build candidate
2
Reconstruct it
3
Measure D and R
4
Compute J
Practical encoders prune candidates and may estimate rate or distortion during faster search stages.
Notes: Define the terms slowly. D measures reconstruction error. R represents the coded rate for all syntax associated with the candidate. Lambda converts the bit cost into the same decision scale as distortion. The encoder selects the lowest J. A full evaluation can build and reconstruct a candidate, obtain distortion, simulate entropy coding, and compute the cost. Practical encoders also use fast approximations and early pruning because exhaustive evaluation is expensive. HEVC standardizes the bitstream and decoder behavior, but it does not mandate one encoder search algorithm.
[Slide-specific evidence]
Chapter 17, Sections 17.1 and 17.2. Rate-Distortion Optimization is an encoder design method, not a normative decoder operation.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 40
Block X decision at λ = 2
Illustrative values show why the lowest distortion and the lowest rate do not necessarily win
Sources and evidence: speaker notes
40 / 49
Option | Candidate description | D: distortion | R: bits | λR | J = D + λR
A | Large Coding Unit, simple mode | 18 | 6 | 12 | 30
B | Smaller Coding Units, better prediction | 8 | 10 | 20 | 28
C | Deep split, many flags | 5 | 16 | 32 | 37
A uses the fewest bits
C has the lowest distortion
B has the lowest combined cost
Option B wins because 28 is the lowest J. The numbers are a teaching example, not an encoder measurement.
Notes: Calculate each row. At lambda two, Option A costs eighteen plus two times six, which equals thirty. Option B costs eight plus two times ten, which equals twenty-eight. Option C costs five plus two times sixteen, which equals thirty-seven. Option A minimizes rate. Option C minimizes distortion. Option B minimizes the combined cost and therefore wins. Do not call B Block X's actual encoder decision. These values were chosen to teach the comparison and were not measured from an HEVC encoder.
[Slide-specific evidence]
Chapter 17, worked Rate-Distortion Optimization example. Values are explicitly illustrative.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 41
Increasing λ changes the preferred candidate
A larger lambda makes every additional coded bit contribute more to the total cost
Sources and evidence: speaker notes
41 / 49
Option | D | R | J when λ = 2 | J when λ = 5 | Result at λ = 5
A | 18 | 6 | 30 | 18 + 5×6 = 48 | WINNER
B | 8 | 10 | 28 | 8 + 5×10 = 58 | 
C | 5 | 16 | 37 | 5 + 5×16 = 85 | 
λ = 2
Option B
λ = 5
Option A
Higher λ shifts the decision toward lower-rate candidates
Lambda normally grows as Quantization Parameter increases, but its exact mapping is encoder-specific.
Notes: Repeat the arithmetic with lambda five. Option A costs forty-eight, Option B costs fifty-eight, and Option C costs eighty-five, so A wins. This matches the role of lambda: a larger value places a larger cost on each additional bit. In practical hybrid video encoders, lambda usually grows roughly exponentially with Quantization Parameter because the quantization step grows exponentially. The leading constant and frame-type adjustments are encoder choices rather than universal normative HEVC rules.
[Slide-specific evidence]
Chapter 17, lambda sensitivity. Exact lambda mapping depends on encoder implementation and coding configuration.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 42
How the encoder obtains the rate term R
R includes the complete syntax cost of a candidate, not only its nonzero transform coefficients
Sources and evidence: speaker notes
42 / 49
COMPLETE CANDIDATE RATE
Partition syntax
Coding Unit and Transform Unit split flags
Prediction syntax
mode, reference index, and motion information
Residual syntax
significance, levels, signs, and end positions
Other syntax
parameters required by the selected coding path
TWO COMMON WAYS TO OBTAIN R
FULL RDO
Simulate entropy coding and count the candidate's coded cost
More accurate, more computation
FAST SEARCH
Estimate syntax cost from context probabilities and simplified models
Faster, but approximate
The earlier 16-bit CABAC tag covered a simplified coefficient-bin example. It was not the complete R for Block X.
Notes: Rate includes every syntax element that changes with the candidate: partition flags, prediction mode, motion information, transform structure, coefficient significance, levels, signs, and related syntax. A full Rate-Distortion Optimization evaluation can run an entropy-coder simulation and accumulate fractional or final bit cost using the current CABAC context state. Faster searches often estimate this cost. The earlier sixteen-bit binary tag represented an idealized arithmetic-coding result for the supplied nineteen-bin coefficient example. It did not include all Block X syntax and should not be presented as the complete candidate rate.
[Slide-specific evidence]
Chapter 15, CABAC; Chapter 17, rate estimation. Practical encoders use exact or estimated entropy costs depending on search stage.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 43
Block X teaching calculation for distortion D
Under an orthonormal transform model, squared coefficient error equals squared spatial-domain error
Sources and evidence: speaker notes
43 / 49
ORIGINAL COEFFICIENTS
42
-12
4
1
-9
5
-2
0
3
-1
1
0
1
0
0
0
−
DEQUANTIZED
40
-16
8
0
-8
8
0
0
0
0
0
0
0
0
0
0
=
COEFFICIENT ERROR
2
4
-4
1
-1
-3
-2
0
3
-1
1
0
1
0
0
0
Square every error and add
2² + 4² + (−4)² + 1² + (−1)² + (−3)² + (−2)² + 3² + (−1)² + 1² + 1²
STEP 8
D = 63
COARSER STEP 16
D = 159
Teaching caveat: HEVC's scaled integer transform requires consistent normalization before using this shortcut.
Notes: Subtract the dequantized coefficient block from the original coefficient block to obtain the displayed error matrix. Square and sum its nonzero entries to obtain sixty-three for quantization step eight. As a self-check, requantizing the original coefficients with step sixteen produces dequantized nonzero values forty-eight, minus sixteen, and minus sixteen. The corresponding squared errors sum to one hundred fifty-nine, so the coarser step increases distortion. Parseval's theorem makes coefficient-domain squared error equal to spatial-domain squared error for an orthonormal transform. HEVC uses scaled integer transforms rather than a mathematically exact orthonormal DCT, so a real encoder must apply consistent scaling or compute distortion after reconstruction.
[Slide-specific evidence]
Chapter 13, transform orthogonality; Chapter 17, distortion. Parseval-based shortcut shown with an explicit normalization caveat. Step-16 value is a teaching calculation.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 44
RDO resolves the encoder's local structural choices
Rate–Distortion Optimization is the common comparison framework, while rate control sets the operating quality target
Sources and evidence: speaker notes
44 / 49
1
CODING UNIT (CU)
Compare the unsplit Coding Unit with legal split trees. Keep the lowest-cost structure.
2
PREDICTION UNIT (PU)
Compare legal partitions, intra or inter modes, references, and motion descriptions.
3
TRANSFORM UNIT (TU)
After prediction, compare legal residual transform trees. PU and TU boundaries may differ.
4
QUANTIZATION PARAMETER (QP)
Fixed QP, Constant Rate Factor, or bitrate control sets the base operating point. Local QP changes may also be optimized.
QP sets the operating region and influences λ. RDO then compares legal candidates around that operating point.
Practical encoders use pruning and heuristics, so they seek a strong solution without evaluating every legal combination.
Notes: Return to the four open questions. Rate-Distortion Optimization compares whether a Coding Unit remains whole or splits. It compares legal Prediction Unit partitions and prediction choices. It compares independent Transform Unit structures for the resulting residual. Quantization Parameter needs a two-layer answer: the application or rate-control system establishes the base operating point through fixed QP, Constant Rate Factor, or a bitrate target; local optimization can then test permitted QP adjustments. QP also influences lambda. RDO forms the encoder's common local decision framework, but practical implementations combine it with search pruning and heuristics rather than evaluating every legal combination.
[Slide-specific evidence]
Chapter 17, Sections 17.1 to 17.4; Chapter 14, Quantization Parameter and rate control. x265 documentation for Constant Rate Factor and bitrate modes.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 45
How bitrate rate control selects a working QP
Quantization Parameter (QP) is chosen before encoding, then the model learns from the measured result
Sources and evidence: speaker notes
45 / 49
1
SET TARGET
Bitrate, frame budget, and buffer constraints
2
ESTIMATE
Use earlier frames, frame complexity, and optional lookahead
3
CHOOSE QP
Select a starting QP for the current picture or region
4
ENCODE
The encoder produces a real number of bits
5
UPDATE
Measured bits and distortion refine the model
FEEDBACK LOOP
The controller predicts first, measures afterward, and corrects the next decision—similar to a thermostat with a content model.
HEVC defines how QP affects decoding; the standard does not require one universal encoder rate-control algorithm.
Notes: Resolve the Quantization Parameter open question in two layers. In fixed-QP mode, the application supplies the value directly. In bitrate-controlled encoding, the controller begins with a target and buffer constraints, estimates a useful QP from earlier coding results and current-frame complexity, encodes the picture, measures the real bits, and updates its model. Some encoders also use lookahead. Therefore rate control is neither a perfect one-time calculation nor purely blind reaction. It is a predictive feedback loop. HEVC standardizes the QP-dependent decoding process, but encoder QP-selection policy is implementation-specific.
[Slide-specific evidence]
Rate-control teaching model. HM reference software exposes picture-QP estimation through estimatePicQP and rate-control state: https://hevc.hhi.fraunhofer.de/HM-doc/_t_enc_g_o_p_8cpp_source.html and https://hevc.hhi.fraunhofer.de/HM-doc/_t_enc_rate_ctrl_8h.html. x265 rate-control modes: https://x265.readthedocs.io/en/stable/cli.html.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 46
Illustrative rate-control feedback: one frame at a time
Target = 1000 bits per frame; positive running balance means the encoder has overspent overall
Sources and evidence: speaker notes
46 / 49
Frame | QP used | Actual bits | Frame error (actual − 1000) | Running balance | QP chosen next
1 | 30 | 1300 | +300 | 0 + 300 = 300 | 32
2 | 32 | 950 | −50 | 300 − 50 = 250 | 32
3 | 32 | 1100 | +100 | 250 + 100 = 350 | 33
4 | 33 | 850 | −150 | 350 − 150 = 200 | 32
CAUSE → EFFECT: overspend raises pressure for a coarser QP; underspend reduces that pressure. The next QP also depends on content and controller policy.
This is a deliberately simple teaching controller—not the normative HEVC algorithm and not a promise that every QP change produces the shown bit count.
Notes: Read the table row by row. Frame one starts from a guessed QP of thirty and costs thirteen hundred bits, so the controller is three hundred bits over budget. It raises QP to thirty-two. Frame two costs nine hundred fifty bits, reducing the cumulative overspend to two hundred fifty, so the toy controller holds QP. Frame three overspends again and the balance rises to three hundred fifty, so it raises QP to thirty-three. Frame four underspends and reduces the balance to two hundred, so the teaching policy eases back to QP thirty-two. Emphasize that QP used in each row was selected before that frame was encoded. The actual bits are learned afterward. Real controllers also consider predicted complexity, buffer fullness, frame type, and other constraints.
[Slide-specific evidence]
Illustrative feedback arithmetic supplied by the user, corrected and labeled as a teaching model. General implementation context: HM reference rate control and x265 rate-control documentation.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 47
Continue the feedback example: what happens at frame 5?
The arithmetic is definite; the next control action requires a stated policy
Sources and evidence: speaker notes
47 / 49
FRAME 5 INPUT
QP used = 32
Actual bits = 1050
UPDATE
Frame error
1050 − 1000 = +50
NEW BALANCE
200 + 50
= 250 bits over
WHAT QP SHOULD FRAME 6 USE?
RAISE
if the controller reacts strongly to any positive overspend
HOLD
if 250 bits lies inside its tolerance band
LOWER
only if complexity prediction or another constraint justifies it
Answer for the arithmetic: +50 this frame and +250 overall. A unique next QP cannot be inferred until the controller rule is specified.
Notes: Ask the audience to calculate before revealing the result. Frame five spends one thousand fifty bits against a one-thousand-bit target, so its error is plus fifty. Add this to the previous running balance of two hundred to obtain two hundred fifty bits over budget overall. The arithmetic is unique. The next QP is not unique from these numbers alone. A simple tolerance-band controller might hold at thirty-two, while a more aggressive controller might raise it. A model-based controller may also incorporate predicted complexity and buffer constraints. This distinction separates measured state from control policy.
[Slide-specific evidence]
Continuation of the supplied teaching example. The non-unique next action is an explicit control-policy caveat.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 48
Block X's journey through the High Efficiency Video Coding (HEVC) encoder
Sources and evidence: speaker notes
48 / 49
1 PARTITION
Select one leaf CU
2 PREDICT
Use a reference and motion vector
3 RESIDUAL
Subtract from the same CU
4 COMPRESS
Transform, quantize, then code
5 RECONSTRUCT
Add the signed decoded residual
The filtered reconstruction becomes the reference used for future inter prediction
Every panel follows the same selected Coding Unit from partition to reconstruction
Notes: Use this as the complete synthesis narration. The encoder begins with a Coding Tree Unit. This teaching example uses a sixty-four-by-sixty-four luma workspace. It recursively tests Coding Unit splits and accepts extra split syntax only when the improved coding result justifies the cost. Each final Coding Unit receives prediction information. Intra prediction uses previously reconstructed neighboring samples and one of the available spatial modes. Inter prediction references already decoded pictures and describes displacement through motion information. A B picture may reference a picture that lies later in display order but has already been decoded. The encoder subtracts the prediction from the source samples to produce a signed residual. Transform Units partition that residual independently of Prediction Unit boundaries. The transform often concentrates correlated residual energy into fewer important coefficients. Quantization rounds these coefficients and creates most of the irreversible coding loss. Quantization Parameter controls its strength. Context-Adaptive Binary Arithmetic Coding then represents partition flags, modes, motion information, transform syntax, and quantized coefficients. In parallel, the encoder dequantizes and inverse-transforms the coefficients, adds the prediction, applies deblocking followed by Sample Adaptive Offset, and stores the result as a reference. Reconstructing locally keeps the encoder's future references consistent with the decoder. Rate-Distortion Optimization supplies a common local comparison using J equals D plus lambda R. Practical encoders prune candidates and use heuristics, while fixed-QP or rate-control policy establishes the base Quantization Parameter. Residual panels in this slide display magnitude for visibility, but coding and reconstruction use signed values.
[Slide-specific evidence]
Chapter 18 synthesis based on [S1] ITU-T H.265, [S2] Sullivan et al. HEVC overview, [S3] Sze et al. Algorithms and Architectures, and [S4] HEVC Test Model encoder documentation. The 64-by-64 workspace and Block X decisions are teaching choices for this deck.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.

## Slide 49
Block X's numeric journey and evidence status
Every value below belongs to the running teaching example; the next presentation follows these decisions into the bitstream
Sources and evidence: speaker notes
49 / 49
Stage | Block X result used in this deck | Evidence status
Partition | Selected leaf CU with two vertical PUs and four TUs | Illustrative structure; not an encoder trace
Transform | 42, −12, 4, 1 / −9, 5, −2, 0 / 3, −1, 1, 0 / 1, 0, 0, 0 | Supplied coefficient example; remaining positions are zero
Quantization | Step 8 produces 5, −2, 1, −1, 1; 5 of 64 positions remain nonzero | Worked arithmetic from the supplied coefficients
CABAC | Locations, levels, and signs follow residual_coding syntax; CABAC codes each requested bin | Normative syntax order shown; no invented standalone Block X bit string
Reconstruction | Dequantized nonzeros: 40, −16, 8, −8, 8; inverse transform and add prediction | Worked continuation; filters operate on reconstructed pixels
Decision | Coefficient-domain teaching distortion D = 63; A/B/C RDO table uses separate illustrative values | No claim that Option B was Block X's measured encoder decision
Next presentation: how syntax elements, quantized coefficients, and headers form the HEVC bitstream.
Notes: Use this table to separate the internally consistent teaching calculations from claims about a real encoder run. The partition diagram selects one Coding Unit with two vertical Prediction Units and four Transform Units. The coefficient matrix and quantization step are supplied teaching values. Dividing by eight and rounding leaves five nonzero levels. For CABAC, the deck now shows the normative residual_coding order and deliberately does not claim a literal standalone bit string for Block X; exact CABAC output depends on the complete syntax and coder state. Dequantization produces forty, minus sixteen, eight, minus eight, and eight before inverse transform. Comparing the original and dequantized coefficient examples gives a teaching squared error of sixty-three under the stated normalization caveat. The A, B, and C Rate-Distortion Optimization values elsewhere in the deck form a separate illustrative comparison. They do not prove that a real encoder selected Option B for Block X. Close by previewing the next presentation, which will explain how headers, syntax elements, and coded payloads are organized into the High Efficiency Video Coding bitstream.
[Slide-specific evidence]
Block X numbers are supplied and derived teaching data. Normative pipeline and syntax basis: [S1]-[S4]. CABAC syntax: [S1] H.265 residual_coding and CABAC clauses. The D equals 63 result is arithmetic derived from the displayed coefficient lists, not an experimental measurement.
[Core source index]
[S1] ITU-T Recommendation H.265, High efficiency video coding: https://www.itu.int/rec/T-REC-H.265
[S2] G. J. Sullivan, J.-R. Ohm, W.-J. Han, and T. Wiegand, Overview of the High Efficiency Video Coding (HEVC) Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221191: https://doi.org/10.1109/TCSVT.2012.2221191
[S3] V. Sze, M. Budagavi, and G. J. Sullivan, editors, High Efficiency Video Coding: Algorithms and Architectures, Springer, 2014: https://doi.org/10.1007/978-3-319-06895-4
[S4] HEVC Test Model reference software documentation: https://hevc.hhi.fraunhofer.de/HM-doc/
[S5] A. Norkin et al., HEVC Deblocking Filter, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2223053: https://doi.org/10.1109/TCSVT.2012.2223053
[S6] C.-M. Fu et al., Sample Adaptive Offset in the HEVC Standard, IEEE TCSVT 22(12), 2012, DOI 10.1109/TCSVT.2012.2221529: https://doi.org/10.1109/TCSVT.2012.2221529
[S7] x265 documentation: https://x265.readthedocs.io/en/stable/
Evidence rule: numerical teaching examples are illustrative unless the slide-specific evidence identifies a measured experiment.